## Slide 1: In-Network Snoop Ordering for Scalable Shared Memory
Niket Agarwal*, Li-Shiuan Peh+, and Niraj K. Jha*
* Princeton University
+ Massachusetts Institute of Technology

## Slide 2: Outline
INSO: In-Network Snoop Ordering
  INSO Overview
  Making INSO practical
  Evaluation
  Related work

## Slide 3: Snoopy Protocols
Snoopy protocols require “totally-ordered broadcast”
Physical networks
  Buses
  Split-transaction buses
  Hierarchical trees
  All have a single ordering point!

## Slide 4: Totally Ordered Broadcast
Ordering Point
P1
P2
Pn
Req A ordered first
Req B ordered next
Req A reaches processors first
Req B reaches processors next
Totally Ordered Broadcast Network
An ordering point provides a simple way of providing a total order among coherence requests
Req A
Req B

## Slide 5: INSO Overview
P1
P2
Pn
Requests are ordered at interconnect routers
Let’s assume Req A
is ordered ahead
of Req B
Req A reaches all processors first
Req B reaches all processors next
INSO implements a virtually ordered network on top of a physically unordered network
Req A
Req B

## Slide 6: INSO: Snoop-order
Snoop-order (SO): SOs are disjoint monotonically increasing numbers
  E.g. 0, 1, 2, ..
Each router in the network has a snoop-order bank containing a disjoint set of SOs
Various possibilities of distributing SOs among routers
  This talk will present a simple technique

## Slide 7: Simple SO distribution
0,16,..
1,17,..
2,18,..
3,19,..
4,20,..
5,21,..
6,22,..
7,23,..
8,24,..
9,25,..
10,26,..
11,27,..
12,28,..
13,29,..
14,30,..
15,31,..
P/M
P/M
P/M
P/M
P/M
P/M
P/M
P/M
P/M
P/M
P/M
P/M
P/M
P/M
P/M
P/M

## Slide 8: INSO in Action
Cache/Memory
Controller
Snoop-order Bank - 0, ..
Snoop-order Allocator
SO CTR = 0
Req A
Snoop-order Bank - .., ..
A - 0
SO CTR = 1
Req A
Distributed SO assignment at routers and in-order request processing by NIC enables total order of requests in INSO
Network
Requests matching SO counter forwarded
&
SO counter incremented
Requests assigned lowest SO from
SO bank
NIC
Router

## Slide 9: INSO Correctness
Properties of INSO that ensure correctness
  All requests have distinct snoop-orders
  Snoop-order counters are incremented only after receiving the snoop-order they are waiting for
  Unused snoop-orders periodically expire

## Slide 10: Outline
GARNET: Detailed on-chip network model
INSO: In-Network Snoop Ordering
  INSO Overview
  Making INSO practical
  Evaluation
  Related work
INCF: In-Network Coherence Filtering

## Slide 11: Making INSO Practical
Described scheme has practicality issues
  Finite Snoop-orders
  Finite destination buffering*
  Deadlock avoidance*
  Snoop-order expiration
* Discussed in HPCA paper

## Slide 12: Finite Snoop-orders
0,16
1,17
2,18
3,19
4,20
5,21
6,22
7,23
8,24
9,25
10,26
11,27
12,28
13,29
14,30
15,31
P/M
P/M
P/M
P/M
P/M
P/M
P/M
P/M
P/M
P/M
P/M
P/M
P/M
P/M
P/M
P/M
Request assigned lowest SO from
SO bank, i.e. ‘0’
16
Request assigned lowest SO from
SO bank, i.e. ‘16’
0,16

## Slide 13: Finite Snoop-orders
Message class in which requests travel, supports point-to-point ordering
Hence, all routers and NICs receive the snoop-orders in the order in which they were broadcasted
In the previous example, the 2nd ‘0’ is implicitly ‘32’, 3rd ‘0’ is ‘64’, and so on
Effect on routing:
  Adaptive routing cannot be employed for the request message class

## Slide 14: Snoop-order Expiration
Routers with lower snoop-orders might not receive requests very frequently
Could be a performance bottleneck
Solution: Expiration
  Assign an expiration window (W)
  A threshold (T) assigned to every router
  Expire up to ‘T’ snoop-orders as expiration messages if not used

## Slide 15: Router Microarchitecture
VC 1
VC n
VC 2
VC 1
VC n
VC 2
Input buffers
Input buffers
VC allocator
Switch
allocator
Route
computation
Input 1
Input P
Output 1
Output P
PxP Crossbar
switch
Expiration
logic
Snoop-order
selector
Snoop-order
bank
Expiration network

## Slide 16: Outline
GARNET: Detailed on-chip network model
INSO: In-Network Snoop Ordering
  INSO Overview
  Making INSO practical
  Evaluation
  Related work
INCF: In-Network Coherence Filtering

## Slide 17: System Configuration
Simulator | Wisconsin GEMS + Princeton GARNET Full-system execution driven simulation
Cores | 64 in-order SPARC cores
Caches | L1 – Split I&D 32 KB, 2 cycle access L2 – 1 MB per-core, 10 cycle access
On-chip Network | 4x4 2D Mesh, 16-byte links 4-cycle router pipeline Idealized VCTM (hardware multicast support)
Memory | 4 memory controllers, 275-cycle DRAM access
Coherence Protocol | Snoopy INSO INSO Oracle (ideal INSO) Directory Protocol
INSO Parameters | Number of SOs-per-router = 64 Contention-less expiration network

## Slide 18: Results: Normalized Runtime
Chart: Normalized Runtime
| fft | lu-c | lu-nc | radix | water-nsq | fmm | blackscholes | swaptions | fluidanimate | vips | Average | splash avg | parsec avg | avg
INSO-Oracle | 0.79 | 0.69 | 0.68 | 0.75 | 0.68 | 0.73 | 0.79 | 0.77 | 0.81 | 0.76 | 0.785
INSO | 0.81 | 0.73 | 0.7 | 0.77 | 0.78 | 0.75 | 0.83 | 0.84 | 0.88 | 0.9 | 0.799
Better
INSO-Oracle
22% better
INSO
20% better
Directory

## Slide 19: Results: Normalized Traffic
Chart: Normalized Traffic
| fft | lu-c | lu-nc | radix | water-nsq | fmm | blackscholes | swaptions | fluidanimate | vips | Average
INSO-Oracle | 2.56 | 2.84 | 2.77 | 3.2 | 2.51 | 2.06 | 2.86 | 2.91 | 3.12 | 2.88 | 2.771
INSO | 2.6 | 2.87 | 2.79 | 3.24 | 2.52 | 2.08 | 2.99 | 2.98 | 3.21 | 2.97 | 2.825
Expiration Traffic | 1.03 | 1.17 | 1.16 | 1.32 | 1.01 | 0.87 | 1.4 | 1.43 | 1.49 | 1.54 | 1.242
Better
INSO has 2-3X
more traffic due
to broadcasts

## Slide 20: INSO Performance: Summary
Average 20% (up to 30%) lower execution time than Directory protocol
2-3X network traffic compared to Directory protocol
Storage overhead = 64 nodes*64 SOs (12 bits) = 6 KB

## Slide 21: Outline
GARNET: Detailed on-chip network model
INSO: In-Network Snoop Ordering
  INSO Overview
  Making INSO practical
  Evaluation
  Related work
INCF: In-Network Coherence Filtering

## Slide 22: Related Work
Token Coherence [Martin et al., ISCA 2003]
  Token storage overhead and expensive fallback mechanism
UnCorq [Strauss et al., MICRO 2007]
  Response message ordered via logical ring
Intel QPI
  Separate ordering agent at directories
Timestamp Snooping [Martin et al., ASPLOS 2000]
  Huge destination buffering and complex router

## Slide 23: Conclusions
INSO provides a scalable snoopy coherence protocol on unordered networks
Leverages simple snoop-order numbers to achieve logical global ordering
Average 20% (up to 30%) faster than directory protocols
Low storage overhead